## Slide 1: Chapter 10 – Sociotechnical Systems
Lecture 1

## Slide 2: Topics covered
Complex systems
Systems engineering
Systems procurement
System development
System operation

## Slide 3: Systems
Software engineering is not an isolated activity but is part of a broader systems engineering process.
Software systems are therefore not isolated systems but are essential components of broader systems that have a human, social or organizational purpose.
Example
  Wilderness weather system is part of broader weather recording and forecasting systems
  These include hardware and software, forecasting processes, system users, the organizations that depend on weather forecasts, etc.

## Slide 4: The sociotechnical systems stack

## Slide 5: Layers in the STS stack
Equipment
  Hardware devices, some of which may be computers. Most devices will include an embedded system of some kind.
Operating system
  Provides a set of common facilities for higher levels in the system.
Communications and data management
  Middleware that provides access to remote systems and databases.
Application systems
  Specific functionality to meet some organization requirements.

## Slide 6: Layers in the STS stack
Business processes
  A set of processes involving people and computer systems that support the activities of the business.
Organizations
  Higher level strategic business activities that affect the operation of the system.
Society
  Laws, regulation and culture that affect the operation of the system.

## Slide 7: Holistic system design
There are interactions and dependencies between the layers in a system and changes at one level ripple through the other levels
  Example: Change in regulations (society) leads to changes in business processes and application software.
For dependability, a systems perspective is essential
  Contain software failures within the enclosing layers of the STS stack.
  Understand how faults and failures in adjacent layers may affect the software in a system.

## Slide 8: Complex systems
A system is a purposeful collection of inter-related components working together to achieve some common objective.
A system may include software, mechanical, electrical and electronic hardware and be operated by people.
System components are dependent on other system components.
The properties and behaviour of system components are inextricably inter-mingled. This leads to complexity.

## Slide 9: System categories
Technical computer-based systems
  Systems that include hardware and software but where the operators and operational processes are not normally considered to be part of the system. The system is not self-aware.
  Example: A word processor used to write a book.
Socio-technical systems
  Systems that include technical systems but also operational processes and people who use and interact with the technical system. Socio-technical systems are governed by organisational policies and rules.
  Example: A publishing system to produce a book.

## Slide 10: Organizational affects
Process changes
  Systems may require changes to business processes so training may be required. Significant changes may be resisted by users.
Job changes
  Systems may de-skill users or cause changes to the way they work. The status of individuals in an organization may be affected by the introduction of a new system.
Organizational changes
  Systems may change the political power structure in an organization. If an organization depends on a system then those that control the system have more power.

## Slide 11: Socio-technical system characteristics
Emergent properties
  Properties of the system of a whole that depend on the system components and their relationships.
Non-deterministic
  They do not always produce the same output when presented with the same input because the systems’s behaviour is partially dependent on human operators.
Complex relationships with organisational objectives
  The extent to which the system supports organisational objectives does not just depend on the system itself.

## Slide 12: Emergent properties
Properties of the system as a whole rather than properties that can be derived from the properties of components of a system
Emergent properties are a consequence of the relationships between system components
They can therefore only be assessed and measured once the components have been integrated into a system

## Slide 13: Examples of emergent properties
Property | Description
Volume | The volume of a system (the total space occupied) varies depending on how the component assemblies are arranged and connected.
Reliability | System reliability depends on component reliability but unexpected interactions can cause new types of failures and therefore affect the reliability of the system.
Security | The security of the system (its ability to resist attack) is a complex property that cannot be easily measured. Attacks may be devised that were not anticipated by the system designers and so may defeat built-in safeguards.
Repairability | This property reflects how easy it is to fix a problem with the system once it has been discovered. It depends on being able to diagnose the problem, access the components that are faulty, and modify or replace these components.
Usability | This property reflects how easy it is to use the system. It depends on the technical system components, its operators, and its operating environment.

## Slide 14: Types of emergent property
Functional properties
  These appear when all the parts of a system work together to achieve some objective. For example, a bicycle has the functional property of being a transportation device once it has been assembled from its components.
Non-functional emergent properties
  Examples are reliability, performance, safety, and security. These relate to the behaviour of the system in its operational environment. They are often critical for computer-based systems as failure to achieve some minimal defined level in these properties may make the system unusable.

## Slide 15: Reliability as an emergent property
Because of component inter-dependencies, faults can be propagated through the system.
System failures often occur because of unforeseen inter-relationships between components.
It is practically impossible to anticipate all possible component relationships.
Software reliability measures may give a false picture of the overall system reliability.

## Slide 16: Influences on reliability
Hardware reliability
  What is the probability of a hardware component failing and how long does it take to repair that component?
Software reliability
  How likely is it that a software component will produce an incorrect output. Software failure is usually distinct from hardware failure in that software does not wear out.
Operator reliability
  How likely is it that the operator of a system will make an error?
Failures are not independent and they propagate from one level to another.

## Slide 17: Failure propagation

## Slide 18: Non-determinism
A deterministic system is one where a given sequence of inputs will always produce the same sequence of outputs.
Software systems are deterministic; systems that include humans are non-deterministic
  A socio-technical system will not always produce the same sequence of outputs from the same input sequence
  Human elements
    People do not always behave in the same way
  System changes
    System behaviour is unpredictable because of frequent changes to hardware, software and data.

## Slide 19: Success criteria
Complex systems are developed to address ‘wicked problems’ – problems where there cannot be a complete specification.
Different stakeholders see the problem in different ways and each has a partial understanding of the issues affecting the system.
Consequently, different stakeholders have their own views about whether or not a system is ‘successful’
  Success is a judgment and cannot be objectively measured.
  Success is judged using the effectiveness of the system when deployed rather than judged against the original reasons for procuement.

## Slide 20: Conflicting views of success
MHC-PMS designed to support multiple, conflicting goals
  Improve quality of care.
  Provide better information and care costs and so increase revenue.
Fundamental conflict
  To satisfy reporting goal, doctors and nurses had to provide additional information over and above that required for clinical purposes.
  They had less time to interact with patients, so quality of care reduced. System was not a success.
However, managers had better reports
  System was a success from a managerial perspective.

## Slide 21: Systems engineering
Procuring, specifying, designing, implementing, validating, deploying and maintaining socio-technical systems.
Concerned with the services provided by the system, constraints on its construction and operation and the ways in which it is used to fulfil its purpose or purposes.

## Slide 22: Stages of systems engineering

## Slide 23: Systems engineering stages
Procurement (acquisition)
  The purpose of the system is established, high-level system requirements are defined, decisions are made on how functionality is distributed and the system components are purchased.
Development
  The system is developed – requirements are defined in detail, the system is implemented and tested and operational processes are defined.
Operation
  The system is deployed and put into use. Changes are made as new requirements emerge. Eventually, the system is decommissioned.

## Slide 24: Security and dependability considerations
Design options limited by procurement decisions
  Purchased components may make some safeguards impossible to implement.
Human errors made during development may introduce faults into the system.
Inadequate testing may mean faults are not discovered before deployment.
Configuration errors during deployment may introduce vulnerabilities.
Assumptions made during procurement may be forgotten when system changes are made.

## Slide 25: Professional disciplines involved in systems engineering

## Slide 26: Inter-disciplinary working
Communication difficulties
  Different disciplines use the same terminology to mean different things. This can lead to misunderstandings about what will be implemented.
Differing assumptions
  Each discipline makes assumptions about what can and can’t be done by other disciplines.
Professional boundaries
  Each discipline tries to protect their professional boundaries and expertise and this affects their judgments on the system.

## Slide 27: Key points
Socio-technical systems include computer hardware, software and people and are designed to meet some business goal.
Human and organizational factors, such as the organizational structure, have a significant effect on the operation of socio-technical systems.
Emergent properties are properties that are characteristic of the system as a whole and not its component parts.
The fundamental stages of systems engineering are procurement, development and operation.

## Slide 28: Chapter 10 – Sociotechnical Systems
Lecture 2

## Slide 29: System procurement
Acquiring a system (or systems) to meet some identified organizational need.
Before procurement, decisions are made on:
  Scope of the system
  System budgets and timescales
  High-level system requirements
Based on this information, decisions are made on whether to procure a system, the type of system and the potential system suppliers.

## Slide 30: Decision drivers
The state of other organizational systems
The need to comply with external regulations
External competition
Business re-organization
Available budget

## Slide 31: Procurement and development
Some system specification and architectural design is usually necessary before procurement
  You need a specification to let a contract for system development
  The specification may allow you to buy a commercial off-the-shelf (COTS) system. Almost always cheaper than developing a system from scratch
Large complex systems usually consist of a mix of off the shelf and specially designed components. The procurement processes for these different types of component are usually different.

## Slide 32: System procurement processes

## Slide 33: Procurement issues
Requirements may have to be modified to match the capabilities of off-the-shelf components.
The requirements specification may be part of the contract for the development of the system.
There is usually a contract negotiation period to agree changes after the contractor to build a system has been selected.

## Slide 34: Contractors and sub-contractors
The procurement of large hardware/software systems is usually based around some principal contractor.
Sub-contracts are issued to other suppliers to supply parts of the system.
Customer liases with the principal contractor and does not deal directly with sub-contractors.

## Slide 35: Procurement and dependability
Procurement decisions have profound effects on system dependability as these decisions limit the scope of dependability requirements.
For an off-the-shelf system, the procurer has very limited influence on the security and dependability requirements of the system.
For a custom system, considerable effort has to be expended in defining security and dependability requirements.

## Slide 36: System development
Usually follows a plan-driven approach because of the need for parallel development of different parts of the system
  Little scope for iteration between phases because hardware changes are very expensive. Software may have to compensate for hardware problems.
Inevitably involves engineers from different disciplines who must work together
  Much scope for misunderstanding here.
  As explained, different disciplines use a different vocabulary and much negotiation is required. Engineers may have personal agendas to fulfil.

## Slide 37: Systems development

## Slide 38: System requirements definition
Three types of requirement defined at this stage
  Abstract functional requirements. System functions are defined in an abstract way;
  System properties. Non-functional requirements for the system in general are defined;
  Undesirable characteristics. Unacceptable system behaviour is specified.
Should also define overall organisational objectives for the system.

## Slide 39: The system design process
Partition requirements
  Organise requirements into related groups.
Identify sub-systems
  Identify a set of sub-systems which collectively can meet the system requirements.
Assign requirements to sub-systems
  Causes particular problems when COTS are integrated.
Specify sub-system functionality.
Define sub-system interfaces
  Critical activity for parallel sub-system development.

## Slide 40: Requirements and design
Requirements engineering and system design are inextricably linked.
Constraints posed by the system’s environment and other systems limit design choices so the actual design to be used may be a requirement.
Initial design may be necessary to structure the requirements.
As you do design, you learn more about the requirements.

## Slide 41: Requirements and design spiral

## Slide 42: Sub-system development
Typically parallel projects developing the hardware, software and communications.
May involve some COTS (Commercial Off-the-Shelf) systems procurement.
Lack of communication across implementation teams can cause problems.
There may be a bureaucratic and slow mechanism for proposing system changes, which means that the development schedule may be extended because of the need for rework.

## Slide 43: System integration
The process of putting hardware, software and people together to make a system.
Should ideally be tackled incrementally so that sub-systems are integrated one at a time.
The system is tested as it is integrated.
Interface problems between sub-systems are usually found at this stage.
May be problems with uncoordinated deliveries of system components.

## Slide 44: System delivery and deployment
After completion, the system has to be installed in the customer’s environment
  Environmental assumptions may be incorrect;
  May be human resistance to the introduction of a new system;
  System may have to coexist with alternative systems for some time;
  May be physical installation problems (e.g. cabling problems);
  Data cleanup may be required;
  Operator training has to be identified.

## Slide 45: Development and dependability
Decisions are made on dependability and security requirements and trade-offs made between costs, schedule, performance and dependability.
Human errors may lead to the introduction of faults into the system.
Testing and validation processes may be limited because of limited budgets.
Problems in deployment mean there may be a mismatch between the system and its operational environment.

## Slide 46: System operation
Operational processes are the processes involved in using the system for its defined purpose.
For new systems, these processes may have to be designed and tested and operators trained in the use of the system.
Operational processes should be flexible to allow operators to cope with problems and periods of fluctuating workload.

## Slide 47: Human error
Human errors occur in operational processes that influence the overall dependability of the system.
Viewing human errors:
  The person approach makes errors the responsibility of the individual and places the blame for error on the operator concerned. Actions to reduce error include threats of punishment, better training, more stringent procedures, etc.
  The systems approach assumes that people are fallible and will make mistakes. The system is designed to detect these mistakes before they lead to system failure. When a failure occurs, the aim is not to blame an individual but to understand why the system defenses did not trap the error.

## Slide 48: System defenses
To improve security and dependability, designers should think about the checks for human error that should be included in a system.
As I discuss in later lectures, there should be multiple (redundant) barriers which should be different (diverse)
No single barrier can be perfect.
  There will be latent conditions in the system that may lead to failure.
However, with multiple barriers, all have to fail for a system failure to occur.

## Slide 49: Reason’s Swiss cheese model of system failure

## Slide 50: Defenses in an ATC system
Conflict alert system
  Raises an audible alarm when aircraft are on conflicting paths
Recording of instructions
  Allows instructions issues to be reviewed and checked.
Sharing of information
  The team of controllers cross-check each other’s work.

## Slide 51: System evolution
Large systems have a long lifetime. They must evolve to meet changing requirements.
Evolution is inherently costly
  Changes must be analysed from a technical and business perspective;
  Sub-systems interact so unanticipated problems can arise;
  There is rarely a rationale for original design decisions;
  System structure is corrupted as changes are made to it.
Existing systems which must be maintained are sometimes called legacy systems.

## Slide 52: Evolution and dependability
Changes to a system are often a source of problems and vulnerabilities.
Changes may be made without knowledge of previous design decisions made for security and dependability reasons.
  Built-in safeguards may stop working.
New faults may be introduced or latent faults exposed by changes.
  These may not be discovered because complete system retesting is too expensive.

## Slide 53: Key points
System procurement covers all of the activities involved in deciding what system to buy and who should supply that system.
System development includes requirements specification, design, construction, integration and testing.
When a system is put into use, the operational processes and the system itself have to change to reflect changing business requirements.
Human errors are inevitable and systems should include barriers to detect these errors before they lead to system failure.